## Slide 1
Floodplain Management Ascension Parish
Marcia Shivers, CFM
Floodplain Manager
Ascension 2026

## Slide 2
Floodplain 101
Base or 1% Flood:
A flood having a 1% chance of being equaled or exceeded in any given year; more commonly referred to as the 100-yr flood.
Common misconception of“100-yr flood” - Does not mean that you will flood once every 100 years.

## Slide 3: Floodplain 101
Base Flood Elevation (BFE):
The height above sea level to which flood water would be expected to rise n a base, or 100-yr flood event.

## Slide 4: FIRM
Ascension Flood Insurance Rate MAP
9/2/1981 – First Effective FIRM issued
1/20/1993 – Map Change
8/16/2007 – Map Change
The 2007 Map Change was probably the most dramatic map change that the Parish has experienced to date. many think that the 2007 FIRM’s are a result of Hurricane Katrina. However, the Parish was already on schedule to have a map change well before this event in 2005.Katrina only delayed the maps from coming out sooner.

## Slide 5: FIRM
Ascension Flood Insurance Rate MAP
Special Flood Hazard Areas (SFHA) = areas subject to flooding during the base flood event
Ascension has 3 types of SFHA’s depicted on the FIRMs.
Zone A – no BFEs determined
Zones AE and AH – BFEs determined

## Slide 6: FIRM
Map changes are inevitable over time.
As we are one of the fastest growing Parishes in the state, this means that not only is our population growing, but development is as well. Due to factors such as increased development and watershed changes over time, SFHAs and BFEs are likely to expand and increase.

## Slide 7: What is the NFIP?
Who
Voluntary and mutual agreement between the Federal Emergency Management Agency (FEMA) and a community.
Participating Communities agree to adopt and administer appropriate regulations – in return all of their residents are eligible for federally-subsidized flood insurance.

## Slide 8: What is the National Flood Insurance Program?
What Happens if a Community does not Participate n the NFIP?
NFIP flood insurance will not be available.
No federal grants, loans, or mortgages for development may be made in identified flood hazard areas.
Makes financing a home extremely difficult and costly.
No federal disaster assistance may be provided to repair insurable buildings located in identified flood hazard areas for damage caused by a flood.

## Slide 9: What is the National Flood Insurance Program?
Ascension Parish and the NFIP
4/26/1973 – entered into the Emergency Phase of NFIP
with no flood map
12/12/1978 – Flood Hazard Boundary Map (FHBM) issued
9/2/1981 – entered into Regular Phase of NFIP and first
effective Flood Insurance Rate Map (FIRM) issued
11/19/1992 – Parish adopts Flood Damage Prevention
Ordinance (minimum NFIP regulations)
4/15/1993 – Parish adopts Building Codes - Permitting
4/17/1997 – Parish adopts 1’ freeboard into the Flood
Damage Prevention Ordinance
09/26/2019 – Parish adopts a 2’ freeboard into the Flood
Damage Prevention Ordinance
Who

## Slide 10: Flood Damage Prevention Ordinance
A community’s floodplain management program and permit records are reviewed periodically by FEMA
Community Assistance Visit (CAV) – conducted every 5 years by FEMA and State NFIP Coordinator’s office (3 years depending on number of policies in force)
If a community is found to not be fully enforcing its Flood Ordinance, their participation in NFIP could be jeopardized

## Slide 11: What is the Community Rating System (CRS)
A voluntary program. Participating communities can get credits for implementing certain activities above and beyond the minimum requirements of NFIP. Residents can get a certain percent reduction in their flood insurance premium rates based on the credits their community earns.

## Slide 12: What is the Community Rating System (CRS)
Goal is to reduce flood losses, insurance ratings, and promote awareness of flood insurance
Uses Class Rating System from 10 to 1 to determine % of flood insurance premium reduction for the community.
Class 10 receives 0% reduction
Class 1 receives maximum of 45% reduction
Activity Categories:
Public Information
Mapping and Regulations
Flood Damage Reduction
Flood Preparedness

## Slide 13: What is the Community Rating System (CRS)
Currently rated as an “7”
Residents receive automatic 15% discount on flood policies, which results in:
-Average Savings of $$80 per policy
-Average Savings of $800,125 Parish-wide
5 Year recertification (on hold due to Federal Government)

## Slide 14: FREEBOARD
An additional height requirement above BFE that provides a margin of safety against extraordinary or unknown risks usually ranges from 1 to 3 feet
Ascension Parish currently has a 2 foot of Freeboard in it’s Flood Damage Prevention Ordinance (adopted 2019)
A 2’ Freeboard results in an average savings of 46% percent on a flood insurance policy, compared to a structure built at BFE

## Slide 15: FREEBOARD
Benefits of Freeboard to Residents
Dramatic savings on insurance premiums
Being able to return to a safe and dry home after a base flood event
Likely to still be at or above a new BFE if ever another map change occurs

## Slide 16: FREEBOARD
Benefits of Freeboard to Ascension Parish
Freeboard is about more than just receiving CRS credits!
Enhanced public safety
Reduction in damages to property and public infrastructure
Avoidance of economic disruption and loss during a storm event
Protects against non-compliant structures which could jeopardize the Parish’s participation in NFIP

## Slide 17: FREEBOARD
Benefits of Freeboard to Ascension Parish
Keep in mind that an event greater than a 100-yr storm can occur at any time and having freeboard is just a little bit of extra “insurance” in ensuring that our residents and their homes and property are safe and protected.

## Slide 18
INSURANCE
NFIP policies in force 9,466 of these 9,236 are Residential and 230 are Non-Residential
$2,733,090.00 Insurance in Force
Average Coverage (Calculated) $288,727
Flood Insurance Stats – Ascension Parish
( As of October 2025)
SFHA
B, C, & X (non-SHFA)
# of Buildings | # of Policies | % (Calculated)
# of Buildings | # of Policies | % (Calculated)
54,032 | 5,387 | 10%
30,045 | 4,079 | 14%

## Slide 19
INSURANCE
Anyone living in a participating community can purchase
flood insurance, whether their building is in a SFHA
or not.
2 types of structures considered:
  Pre-FIRM – constructed before the date of the initial
  FIRM of the community (Ascension Parish- prior to
  9/2/1981) Pre-FIRM structures are treated and rated differently than structures built Post-FIRM – rates not “actuarial”
  Post-FIRM – rated based on how protected they are
  from the mapped hazard (ex. slab height in feet above
  or below BFE) – Ascension Parish – 9/2/1981 to present
Flood Insurance Stats – Ascension Parish
( As of October 2025)
Pre-FIRM vs Post-FIRM Policies
Pre-FIRM Post-FIRM
SFHA B, C, & X SFHA B, C, & X
781 456 3,298 4,924

## Slide 20: Flood Facts
Every year, flooding causes more than $2 billion of property damage in the U.S.
In a high risk area, your home has a 26% chance of being damaged by a flood during the course of a 30-year mortgage, compared to a 9% chance of fire.
Source: FloodSmart.gov

## Slide 21: Flood Facts
PROTECT YOURSELF WITH FLOOD INSURANCE
Get information on your flood risk and prepare with an emergency plan, which should include purchasing flood insurance to protect property and possessions from flood damage.
Remember, most homeowners insurance does not cover floods, and there typically is a 30-day wait before a policy goes into effect. If you already have a flood policy, be sure to renew it each year to remain financially protected against costly flood damage.
A flood can be devastating, and you don't have to live near water to be at risk. Factors such as changing weather patterns or land development can present new flooding risks for your community.
Only 6 inches of flood water can cause over $20,000 in damage to a 1,000 sq. ft. home.
In high-risk areas, there is at least a 1 in 4 chance of flooding during a 30-year mortgage.
Homeowners can insure a home for up to $250,000 and its contents for up to $100,000. Renters can cover their belongings for up to $100,000. Non-residential property owners can insure a building and its contents for up to $500,000 each.

## Slide 22
Floodplain Management Ascension Parish
Marcia Shivers
Floodplain Manager
225-450-1002
Marcia.Shivers@apgov.us